This doc explains the CPSW driver for am33x EVM. For this the docs are placed in Network/Docs/AM33XX.
Following things are available on the board with respect to ethernet:
1. The PHY used is the Atheros AR8031_AL1A.
2. The MII interface is RGMII interface.
Following the signals used for the RGMII interface between MAC and PHY:

Let's now understand from the driver perspective. There is a function called rgmii1_init in board-am335xevm.c. This just sets the pin multiplexing for the RGMII mode. After that we invoke the am33xx_cpsw_init in arch/arm/mach-omap2/devices.c. The first thing which it does is to read the mac address from the control registers and initialize the am33xx_cpsw_slaves, then we set the phy mode to RGMII and the corresponding interface in MAC. Then we look up for the module mdio and build the device with name davinci_mdio with platform data of 16Mhz speed. The corresponding driver is located at drvers/net/ethernet/ti/davinci_mdio.c. Next step is to look for CPGMAC0 hw module and the device registered is cpsw. The corresponding driver is at net/ethernet/ti/cpsw.c.
Looking at the datasheet, it shows that it consists of following:
CPSW_SS - Ethernet switch sub system
CPSW_PORT – Ethernet Switch port control
CSPW_CPDMA – CPPI DMA controller module
CPSW_STATS – Ethernet statistics
CPSW_STATE_RAM – DMA state RAM
CPSW_CPTS – Time sync module
ALE – Address Lookup Engine
SL1 – Sliver for port 1
SL2 – Silver for port 2
MDIO – Ethernet MDIO controller
CPSW_WR – Wrapper for RMII/RGMII

As per my understanding, the TRM says that the Ethernet subsystem consists of 2 GMII interface modules and 2 RGMII modules.

In arch/arm/mach-omap2/omap_hwmod_33xx_data.c, there is a hw module called cpgmac0 whose structure is defined as below:
static struct omap_hwmod am33xx_cpgmac0_hwmod = {
        .name = "cpgmac0",
        .class = &am33xx_cpgmac0_hwmod_class,
        .clkdm_name = "cpsw_125mhz_clkdm",
        .mpu_irqs = am33xx_cpgmac0_irqs,
        .main_clk = "cpgmac0_ick",
        .prcm = {
        .omap4 = {
        .clkctrl_offs = AM33XX_CM_PER_CPGMAC0_CLKCTRL_OFFSET,
        .modulemode = MODULEMODE_SWCTRL,
        },
        },
        .slaves = am33xx_cpgmac0_slaves,
        .slaves_cnt = ARRAY_SIZE(am33xx_cpgmac0_slaves),
        .flags = (HWMOD_SWSUP_SIDLE | HWMOD_SWSUP_MSTANDBY |
        HWMOD_SWSUP_RESET_BEFORE_IDLE),
};
The cpsw platform device is created as a part of cpsw_init. The platform data for this device as follows:

static struct cpsw_platform_data am33xx_cpsw_pdata = {
        .ss_reg_ofs = 0x1200,
        .channels = 8,
        .cpdma_reg_ofs = 0x800,
        .slaves = 2,
        .slave_data = am33xx_cpsw_slaves,
        .ale_reg_ofs = 0xd00,
        .ale_entries = 1024,
        .host_port_reg_ofs = 0x108,
        .hw_stats_reg_ofs = 0x900,
        .cpts_reg_ofs = 0xc00,
        .cpts_clock_mult = 0x80000000,
        .cpts_clock_shift = 29,
        .bd_ram_ofs = 0x2000,
        .bd_ram_size = SZ_8K,
        .rx_descs = 64,
        .mac_control = BIT(5), /* MIIEN */
        .gigabit_en = 1,
        .host_port_num = 0,
        .no_bd_ram = false,
        .version = CPSW_VERSION_2,
};

It consists of offsets for various things such as ss_regs_off, ale_regs_ofs, host_port_regs_off, hw_stats_regs_off, cptfs_regs_ofs. Apart from this the number of channels, num of slaves, rx_descs and so on. This is passed to cpsw driver.
The probe function cpsw_probe (/net/ethernet/ti/cpsw.c) does the following things:
1. Alloc the etherdev device with cpsw_private as the private data for the same.
2. Then we go about initializing the various fields such as pointer to platform data, allocate the time sync structure
3. Allocate the slaves
4. Then, we go about getting the base addresses of SS (switch subsystem)and WR (wrapper subsystem).
5. Get the virtual address for the SS (2K) and WR (256) registers
6. Then, we go about initializing the address for the slave ports
7. We request the timer 5 and 6 for rx and tx.
8. Next step is to initialize the dma register params which contains the offsets for various DMA registers. Then, we initialize the number of channels, ram size (8K) here. After initializing all these parameters, we go about calling the cpdam_ctl_create.
9. Then, we initialize the tx and rx ch for dma
10. Then, initialize the Address Look up enable
11. Next we go about initializing the irqs which are following:
static struct omap_hwmod_irq_info am33xx_cpgmac0_irqs[] = {
        { .name = "c0_rx_thresh_pend", .irq = 40 },
        { .name = "c0_rx_pend", .irq = 93 },
        { .name = "c0_tx_pend", .irq = 94 },
        { .name = "c0_misc_pend", .irq = 43 },
        { .irq = -1 }
};
We request the irqs for these and register a handler.