Network Drivers Understanding

Following are the good references:
https://wiki.aalto.fi/download/attachments/70789076/Network_device_drivers_in_Linux_subFinal.pdf?version=1&modificationDate=1355954302000
http://gauss.ececs.uc.edu/Courses/c4029/code/drivers/Kernel/docs.html (Referred for initial study)
http://linuxgazette.net/156/jangir.html (Very Nice Explaination)
http://searchsrikanth.blogspot.in/2010/03/how-to-write-network-driver-in-linux.html (Nice Explaination)
http://www.tldp.org/LDP/LG/issue93/bhaskaran.html (Nice Explaination)
http://free-electrons.com/doc/network-drivers-lab.pdf (Nice Labs for Free Electrons)
Nice network related material is found at free electrons:
http://free-electrons.com/docs/network-drivers/

From Videos on Network subsytem[Networking subystem consists of various folders under net such as core, ipv4, ipv6, bluetooth, bridge, ipx, nfc, netlink. Core consists of all the apis for networking subsystem, Then there are various protocol stacks such as ipv4, ipv6, bluetooth. The most important files under net folder are as below:
dev.c - contains the things related to device registration. The main RX and TX interceps are found here. You will also find here the ring buffers here. Socket.c handles the socket layer kind of thing from user space.
ipv4 contains the protocol stack. In this, some of the important files are ip_input and ip_output. To handle ip based routing you have ip_forward.c. You have icmp to handle the icmp logic. Then there are transport related source code, udp source code.]

My intention was to understand the driver which is currently working on my PC. Its r8169 used by default. Next step was to figure out how driver was written for sysplay. So, downloaded the network driver at Network/Templates/NetworkDriver. Found that its derived from r8101. So, downloaded the original source at /home/expert/Learnings/Network/Templates. Found that the single r8101_n.c is split into phy.c, mac.c, pci_net.c and net_stk.c.

In order to better understand of the driver flows, I referred the following article:
 http://gauss.ececs.uc.edu/Courses/c4029/code/drivers/Kernel/docs.html
This article is also copied as network.pdf in network/docs folder.

As with the characters and block drivers, network drivers too need to register with kernel data structure. However, there are few different things. For characters and block drivers, the device file which in block system represents a partition in a disk, exists as a special file, whereas a network interface has no such entry point. The normal file operations like read, write and so on do make sense when applied to network interface, so its not possible to apply the Unix 'everything is a file” approach to them. Network interface exports a different set of operations. Although you may object that applications use the read and write system calls when using sockets, those calls act on a software object that is distinct from the interface. Several hundred sockets can be multiplexed on the same physical interface.But the most important difference between the two is that block drivers soperate only in response to requests from the kernel, whereas network drivers receive packets
asynchronously from the outside. Thus, while a block driver is asked to send a buffer
toward the kernel, the network device asks to push incoming packets toward the ker-
nel. The kernel interface for network drivers is designed for this different mode of
operation.Network drivers also have to be prepared to support a number of administrative
tasks, such as setting addresses, modifying transmission parameters, and maintain-
ing traffic and error statistics. The API for network drivers reflects this need and,
therefore, looks somewhat different from the interfaces we have seen so far.The network subsystem of the Linux kernel is designed to be completely protocol-
independent. This applies to both networking protocols (Internet protocol [IP] versus
IPX or other protocols) and hardware protocols (Ethernet versus token ring, etc.).
Interaction between a network driver and the kernel properly deals with one network
packet at a time; this allows protocol issues to be hidden neatly from the driver and
the physical transmission to be hidden from the protocol.
Normally, as you understand, when you send a block of data over a TCP socket, the network subsystem breaks that data up into the packets and puts a TCP header at the beggining. Header is nothing but a set of bytes prepended to a packet as it passes through the various layers of the networking subsystem. Tcp header describes where each packet fits within the stream. The lower layers then put an IP header in front of TCP header. It is used to route the packet to its destination. If the packet is moved over an ethernet like medium, an ethernet header, interpreted by hardware, goes in front of rest. Network drivers need not be concerned about the high-level headers, but they often must be involved in creation of hardware-level header.

Now, lets understand the network subsystem. So, there are two things here – one is the Network protocol stack which typically is TCP/IP stack and it interacts with the user space through network interfaces instead of devices, which is typically the case in block and char drivers. Also, here you won't find any entry in /sys or /dev enteries. Interface examples are eth0, wlan0 and in usb ethernet driver, it is usb0. And this resides in <kernel_source>/net folder. And other part is the NIC (Network interface card) driver which is driver for the physical network cards. And, its role is to provide the uniform hardware independent interface for the network protocol layer to access the card. Typically resides in <kernel_source>/drivers/net folder.
So, writing a NIC driver involves interacting with the underlying card over its I/O bus and providing the standard APIs to the protocol stack. So, the interface between the NIC and protocol stack is being provided by struct net_device and that of between hardware card and driver is dependent on type of bus and hence is provided by IO bus specific data structures which can be USB, PCI and so on. The third thing is something called sk_buff which is the core of the protocol stack. Now, as you understand, the task which are performed by the network interfaces are data transmission and data reception. Each packet handled by kernel is contained in a socket buffer structure called sk_buff and gets its name from unix abstraction used to represent a network connection, the socket. We will talk about this latter. This socket buffer is a complex structure and the kernel offers a number of functions to act on this. The fields which are relevant to the driver are head which points to the start of the packet, tail points to the tail of the packet. Data points to the start of the packet payload and end points to the end of packet payload. Len is the amount of data that the packet contains. The socket buffer passed to hard_start_xmit contains the physical packet as it should appear on the media, complete with the transmission-level headers. The interface
doesn’t need to modify the data being transmitted. skb->data points to the packet
being transmitted, and skb->len is its length in octets. So, head, data, tail and end are the pointers used to address the data in the packet. Head point to the beginning of allocated space, data is the beginning of the valid bytes (octets) and is usually slightly greater than the head, tail is the end of the valid data and end points to the maximum address tail can reach. Another way to look at it is that the available buffer space is skb->end - skb->head, and the currently used data space is
skb->tail – skb->data.

Code flow

General data structures

net_device defined in include/linux/netdevice.h. Important fields are :
char name[IFNAMSIZ]
unsigned int irq; /* device IRQ number */
/* currently active device features */
        u32 features;
        /* user-changeable features */
        u32 hw_features;
        /* user-requested features */
        u32 wanted_features;
        /* mask of features inheritable by VLAN devices */
        u32 vlan_features;
/* Interface index. Unique device identifier */
int ifindex;
int iflink;
/* Management operations */
const struct net_device_ops *netdev_ops;
const struct ethtool_ops *ethtool_ops;
/* Hardware header description */
const struct header_ops *header_ops;
unsigned int mtu; /* interface MTU value */
unsigned short type; /* interface hardware type */
unsigned short hard_header_len; /* hardware hdr length */
/* Interface address info. */
unsigned char perm_addr[MAX_ADDR_LEN]; /* permanent hw address */
unsigned char addr_assign_type; /* hw address assignment type */
unsigned char addr_len; /* hardware address length */
unsigned short dev_id; /* for shared network cards */
/* Interface address info used in eth_type_trans() */
unsigned char *dev_addr; /* hw address, (before bcast
because most packets are
unicast) */
1. struct usbnet defined in include/linux/usb/usbnet.h. It is an interface from usbnet core to each USB networking link we handle:
  struct usbnet {
  /* housekeeping */
  struct usb_device *udev;
  struct usb_interface *intf;
  struct driver_info *driver_info;
  const char *driver_name;
  void *driver_priv;
  wait_queue_head_t *wait;
  struct mutex phy_mutex;
  unsigned char suspend_count;
  /* i/o info: pipes etc */
  unsigned in, out;
  struct usb_host_endpoint *status;
  unsigned maxpacket;
  struct timer_list delay;
  /* protocol/interface state */
  struct net_device *net;
  int msg_enable;
  unsigned long data[5];
  u32 xid;
  u32 hard_mtu; /* count any extra framing */
  size_t rx_urb_size; /* size for rx urbs */
  struct mii_if_info mii;
  /* various kinds of pending driver work */
  struct sk_buff_head rxq;
  struct sk_buff_head txq;
  struct sk_buff_head done;
  struct sk_buff_head rxq_pause;
  struct urb *interrupt;
  struct usb_anchor deferred;
  struct tasklet_struct bh;
  struct work_struct kevent;
  unsigned long flags;
  # define EVENT_TX_HALT 0
  # define EVENT_RX_HALT 1
  # define EVENT_RX_MEMORY 2
  # define EVENT_STS_SPLIT 3
  # define EVENT_LINK_RESET 4
  # define EVENT_RX_PAUSED 5
  # define EVENT_DEV_WAKING 6
  # define EVENT_DEV_ASLEEP 7
  # define EVENT_DEV_OPEN 8

        3. struct usb_device – Kernel's representation of usb device. Defined in include/linux/usb.h

struct sk_buff – this is where the packet is stored. This is where a packet is stored. The structure is used by all the network layers to store their headers, information about the user data (the payload), and other information needed internally for coordinating their work.

  - The sk_buff head structure is :
    struct sk_buff_head {
    struct sk_buff *next;
    struct sk_buff *prev;
    u32 qlen;
    spinlock_t lock;
}
qlen defines the number of elements in the list. Lock is used to prevent simultaneous accesses to the list.
        Struct sk_buff: Interesting fields:
struct sock *sk - This is the pointer to the sock data struture of the socket that owns this	buffer
        int len: This is the size of the block of data in the buffer. The len includes both the data in the main buffer and the data in the fragments. Its value changes as the buffer moves from one network layer to the next, because headers are discarded while moving up in the stack and added while moving down in the stack.
        Int data_len: data length only accounts for the size of the data in the fragments.
        Int mac_len – This is the size of mac header

unsigned char *head
unsigned char *end
unsigned char *data - These represent the boundaries of the buffer and the data within it. When each layer prepares the buffer for its activities, it may allocate more space for a header
or for more data. head and end point to the beginning and end of the space allo-
cated to the buffer, and data and tail point to the beginning and end of the
actual data. See Figure 2-2. The layer can then fill in the gap between head and
unsigned char *tail

net_device data structure: it is the structure stores specifically all the information regarding the network device.The fields of the net_device structure can be classified into the following categories:
Refer page 44 in understanding network internals
• Configuration
• Statistics
• Device status
• List management
• Traffic management
• Feature specific
• Generic
• Function pointers (or VFT)

struct net_device
Each network device is represented in the Linux kernel by this data structure,
which contains information about both its hardware and its software configura-
tion. See Chapter 8 for details on when and how net_device data structures are
allocated.

when insmod smsc95xx.ko is invoked, usbnet probe which does the following:
- Gets the driver name in local variable name, stores the driver_info locally. Gets the usb device from the interface in variable xdev. usb_get_device is called, which increments the ref count. Each live reference to a device should be refcounted, when it binds to an interface in probe. Release them by calling usb_put_dev in their disconnect.
  - Then, alloc_etherdev is called which does the following:
    - Allocates and sets up an ethernet device
    - Fills in the fields of device structure with ethernet generic values. Basically does everything except registering the device.
    - Constructs a new net device, complete with a private data area of size (sizeof_priv). A 32-byte (not bit) alignment is enforced for this private data area.
    - Allocates a struct net_device with private data area for driver use and performs basic initialization. Also allocates subquue structs for each queue on the device.
    - It returns a struct of type net_device
      - Then, the private variable allocated in alloc_etherdevice is extracted and various information is filled. Such as interface, name, usb_device, driver_info and so on.
    - Then, it does init_usb_anchor. Explaination of this is given in Kernel/documentation/USB/anchor.txt. A USB driver needs to support some callbacks requiring a driver to cease all IO to an interface. To do so, a driver has to keep track of the URBs it has submitted to know they've all completed or to call usb_kill_urb for them. The anchor is a data structure takes care of keeping track of URBs and provides methods to deal with multiple URBs.
    - Then, it sets up the timeout for the watchdog timer which is actually 5 Hz. Page no. 258 of networking internals.
  - Then, there is skb_queue_head_init. The kernel maintains all the sk_buff structures in the doubly linked list and so like any doubly linked list, it has prev and next pointer. But, this list has another requirement, each sk_buff structure must be able to find head of the whole list quickly. To, implement this requirement, an extra structure of type sk_buff_head is inserted at the beggining of the list, as a kind of dummy element.
  - Then, the tasklet function is assigned to the the bh.function, work queue is initialized.
  - Then the usbnet_ops are registered as netdev_ops. And ethtool_ops are registered.
  - Then the bind is invoked, which is nothing but the smsc95xx_bind and does the device specific initialization.
  - Then, init_status is invoked if dev_status is set( i.e interrupt endpoint is initialized which is done in bind of smsc95xx)which in turn invokes the smsc95xx_status. init_status initialize the pipe for the interrupt endpoint, allocates the interrupt urb and initializes the interrupt urb.usb_set_intfdata is needed since usb driver needs to retrieve the local data structure that is associated with the interface, latter in the lifecycle of the device.
  - register_netdev is used to register a network device. It takes a completed network device structure and add it to the kernel interfaces. This is the wrapper around register_netdevice that takes the rtnl semaphore.
  - netif_device_attach – It is one which is required during the resumption of the device. It sets the link status of the device, because device is now available. If the device was enabled before being suspended, re-enable its egress queue with netif_wake_queue and restart a watchdog timer. Refer p162- understanding network internals.
- Flow for the bind is as follows:
  - It first invokes the usbnet_get_endpoints which intializes the pipes for bulk in and out endpoints. It also stores the interrupt endpoint in status field of usbnet. This will be latter initialized in the int_status.
  - Then, you store the pointer to the device specific i.e. smsc95xx_priv in device data field
  - Then, you initialize the mac address from the eeprom if available. This is done with smsc95xx_init_mac_address. Then, smsc95xx_reset is invoked. Here, the device is first light resetted. Then, we wait for the reset to be completed. Then, we reset the PHY with command PM_CTL_PHY_RST_. Then, it sets the MAC address. smsc95xx_set_mac_address. Then, we set the Bulk in Empty Response (BIR) bit in HW_CFG which controls the response to the Bulk-in token when the RX FIFO is empty. Here, it responds with NAK. Then, we check turbo mode [ The maximum transaction size for bulk-only transfers (BOT) at the operating system level is 64 KB. However, sequential data is typically moved in 128 KB blocks, requiring two BOT transactions. What's being referred to as "Turbo mode" overcomes that limitation by increasing the maximum transfer size to 1 MB or larger, allowing the USB driver to pack several 128 KB sequential requests into one larger transaction. Fewer small transactions means less wait, ready, and acknowledge USB commands, in turn reducing the amount of bandwidth consumed by signal overhead.] and set the packet size. ]. Then, the burst cap is set. BURST_CAP indicates the maximum amount of contiguous data that may be transmitted by UTX before a ZLP is sent. Then, it sets the BULK_IN_Delay which indicates the time, UTX waits for, before sending the short packet. Then, we enable Multiple Ethernet frames per USB packet, which enables packing multiple ethernet frames per USB packet when possible and BCE which enables the use of burst cap register.

Now, what is MII? MII stands for Media independent interface was defined as standard interface used to connect a Fast Ethernet to MAC block to phy chip. In a nutshell, it is an interface between MAC layer and Phy layer. The MII design has been extended to support reduced signals and increased speeds. Current variants are Reduced Media Independent Interface, Gigabit Media Independent Interface, Reduced Gigabit Media Independent Interface, Serial Gigabit Media Independent Interface, 10 Gigabit Media Independent Interface, XAUI, GBIC, SFP, SFF, XFP, and XFI.Being media independent means that different types of PHY devices for connecting to different media (i.e. Twisted pair copper, fiber optic, etc.) can be used without redesigning or replacing the MAC hardware. The MII bus (standardized by IEEE 802.3u) connects different types of PHYs (Physical Transceivers) to Media Access Controllers (MAC).
The MDIO Serial Management Interface (SMI) is used to transfer management information between MAC and PHY. At powerup the PHY usually adapts to whatever it's connected to (Auto-negotiation) unless you alter settings via the MDIO interface.
MII has two signal interfaces:
- A Data interface to the Ethernet MAC, for sending and receiving Ethernet frame data.
- A PHY management interface, MDIO, used to read and write the control and status registers of the PHY which are used to configure each PHY before operation, and to monitor link status during operation.

Functions
skb_queue_head_init
Initializes an sk_buff_head with an empty queue of elements.
skb_queue_head, skb_queue_tail
Adds one buffer to the head or to the tail of a queue, respectively.
skb_dequeue, skb_dequeue_tail
Dequeues an element from the head or from the tail, respectively. The second
function should probably have been called skb_dequeue_head to be consistent
with the names of the other queueing functions.
skb_queue_purge
Empties a queue.
skb_queue_walk
Runs a loop on each element of a queue in turn.
All functions of this class must be executed atomically—that is, they must grab the

When the ifconfig eth0 192.168.20.230 is invoked,